Laurea Specialistica in Ingegneria Spaziale

2° anno

Corso ‘Stazioni di Terra’

Appendice 10

Il Sistema GPS: una sintesi

#### Giorgio Perrotta

Anno accademico 2007

#### Global Positioning System

The Global Positioning System (GPS), is the only fully-functional satellite navigation system. More than two dozen GPS satellites orbit the Earth, transmitting radio signals which allow GPS receivers to determine their location, speed and direction.  Since the first experimental satellite was launched in 1978, GPS has become indispensable for navigation around the world and an important tool for map-making and land surveying. GPS also provides a precise time reference used in many applications including scientific study of earthquakes, and synchronization of telecommunications networks.

Developed by the United States Department of Defense, it is officially named NAVSTAR GPS (Navigation Signal Timing and Ranging Global Positioning System). The satellite constellation is managed by the United States Air Force 50th Space Wing. Although the cost of maintaining the system is approximately US$ 400 million per year, including the replacement of aging satellites, GPS is free for civilian use as a public good.  In late 2005, the first in a series of next-generation GPS satellites was added to the constellation, offering several new capabilities, including a second civilian GPS signal called L2C for enhanced accuracy and reliability. In the coming years, additional next-generation satellites will increase coverage of L2C and add a third and fourth civilian signal to the system, as well as advanced military capabilities. introduction

A GPS receiver calculates its position by measuring the distance between itself and three or more GPS satellites. Measuring the time delay between transmission and reception of each GPS radio signal gives the distance to each satellite, since the signal travels at a known speed. The signals also carry information about the satellites' location. By determining the position of, and distance to, at least three satellites, the receiver can compute its location using trilateration.  Receivers do not have perfectly accurate clocks, and must track one extra satellite to correct their clock error.

##### Satellites and Ground Control

The GPS design calls for 24 satellites to be distributed equally among six circular orbital planes with 55° declination (tilt relative to the equator) and separated by 60° right ascension (angle along the equator). Orbiting at an altitude of 10,988 nautical miles (approximately 20,200 kilometers or 12,600 statute miles), each satellite passes over the same location on Earth twice a day. The orbits are arranged so that at least four satellites are always within line of sight from almost anywhere on Earth.   As of August 2006, there are 29 active satellites in the GPS constellation. The five extra ones are distributed among the six orbital planes, improving the precision of GPS receiver calculations by providing redundant measurements. They also ensure that, should an individual satellite malfunction, enough functional satellites remain in orbit for normal operation.

The flight paths of the satellites are tracked by monitoring stations in Hawaii, Kwajalein, Ascension Island, Diego Garcia and the master control station, at Schriever Air Force Base, Colorado Springs, Colorado where the monitoring stations' combined observations are processed via a Kalman Filter. The 2d Space Operations Squadron of the USAF contacts each GPS satellite regularly with a navigational update (using the ground antennas at Ascension Island, Diego Garcia and Kwajalein). These updates synchronize the atomic clocks on board the satellites to within one microsecond and adjust the ephemeris of each satellite's internal orbital model to match the observations made from the ground, space weather information, and other various inputs.

##### Navigation signals

GPS satellites broadcast three different types of data in the primary navigation signal. The first is the almanac which sends coarse time information along with status information about the satellites. The second is the ephemeris, which contains orbital information that allows the receiver to calculate the position of the satellite. This data is included in the 37,500 bit Navigation Message, which takes 12.5 minutes to send at 50 bps.

The satellites also broadcast two forms of clock information, the Coarse / Acquisition code, or C/A which is freely available to the public, and the restricted Precise code, or P-code, usually reserved for military applications. The C/A code is a 1,023 bit long pseudo-random code broadcast at 1.023 MHz, repeating every millisecond. Each satellite sends a distinct C/A code, which allows it to be uniquely identified. The P-code is a similar code broadcast at 10.23 MHz, but it repeats only once a week. In normal operation, the so-called "anti-spoofing mode", the P code is first encrypted into the Y-code, or P(Y), which can only be decrypted by units with a valid decryption key. Frequencies used by GPS include:

- L1 (1575.42 MHz) - Mix of Navigation Message, coarse-acquisition (C/A) code and encrypted precision P(Y) code.

- L2 (1227.60 MHz) - P(Y) code, and a second C/A code on the Block II-R and newer satellites.

- L3 (1381.05 MHz) - Used by the Defense Support Program to signal detection of missile launches, nuclear detonations, and other high-energy infrared events.

- L4 (1841.40 MHz) - Being studied for additional ionospheric correction.

- L5 (1176.45 MHz) - Proposed for use as a civilian safety-of-life (SoL) signal. This frequency falls into an internationally protected range for aeronautical navigation, promising little or no interference under all circumstances. The first Block IIF satellite that would provide this signal is set to be launched in 2008.

##### Receivers

In general, GPS receivers are composed of an antenna, tuned to the frequencies transmitted by the satellites, receiver-processors, and a highly-stable clock (often a crystal oscillator). They may also include a display for providing location and speed information to the user. A receiver is often described by its number of channels: this signifies how many satellites it can monitor simultaneously. Originally limited to four or five, this has progressively increased over the years such that, as of 2006, receivers typically have between twelve and twenty channels.

GPS receivers come in a variety of formats, from devices integrated into cars, phones, and watches, to dedicated devices such those shown here from manufacturers Trimble, Garmin and Leica (left to right).

GPS receivers may include an input for differential corrections, using the RTCM SC-104 format. This is typically in the form of a RS-232 port at 4,800 bps speed. Data is actually sent at a much lower rate, which limits the accuracy of the signal sent using RTCM. Receivers with internal DGPS receivers can outperform those using external RTCM data. As of 2006, even low-cost units commonly include WAAS receivers.

Many GPS receivers can relay position data to a PC or other device using the NMEA 0183 protocol. NMEA 2000 is a newer and less widely adopted protocol. Both are proprietary and controlled by the US-based National Marine Electronics Association. References to the NMEA protocols have been compiled from public records, allowing open source tools like gpsd to read the protocol without violating intellectual property laws. Other proprietary protocols exist as well, such as the SiRF protocol. Receivers can interface with other devices using methods including a serial connection, USB or Bluetooth.

##### Calculating positions

The coordinates are calculated according to the World Geodetic System WGS84 coordinates system. To calculate its position, a receiver needs to know the precise time. The satellites are equipped with extremely accurate atomic clocks, and the receiver uses an internal crystal oscillator-based clock that is continually updated using the signals from the satellites.

The receiver identifies each satellite's signal by its distinct C/A code pattern, then measures the time delay for each satellite. To do this, the receiver produces an identical C/A sequence using the same seed number as the satellite. By lining up the two sequences, the receiver can measure the delay and calculate the distance to the satellite, called the pseudorange.

Overlapping pseudoranges, represented as curves, are modified to yield the probable position

The orbital position data from the Navigation Message is then used to calculate the satellite's precise position. Knowing the position and the distance of a satellite indicates that the receiver is located somewhere on the surface of an imaginary sphere centered on that satellite and whose radius is the distance to it. When four satellites are measured simultaneously, the intersection of the four imaginary spheres reveals the location of the receiver. Earth-based users can substitute the sphere of the planet for one satellite by using their altitude. Often, these spheres will overlap slightly instead of meeting at one point, so the receiver will yield a mathematically most-probable position (and often indicate the uncertainty).

Calculating a position with the P(Y) signal is generally similar in concept, assuming one can decrypt it. The encryption is essentially a safety mechanism; if a signal can be successfully decrypted, it is reasonable to assume it is a real signal being sent by a GPS satellite. In comparison, civil receivers are highly vulnerable to spoofing since correctly formated C/A signals can be generated using readily available signal generators. RAIM features will not help, since RAIM only checks the signals from a navigational perspective.

##### Accuracy and Error Sources

The position calculated by a GPS receiver requires the current time, the position of the satellite and the measured delay of the received signal. The position accuracy is primarily dependent on the satellite position and signal delay.

To measure the delay, the receiver compares the bit sequence received from the satellite with an internally generated version. By comparing the rising and trailing edges of the bit transitions, modern electronics can measure signal offset to within about 1% of a bit time, or approximately 10 nanoseconds for the C/A code. Since GPS signals propagate nearly at the speed of light, this represents an error of about 3 meters. This is the minimum error possible using only the GPS C/A signal.

Position accuracy can be improved by using the higher-speed P(Y) signal. Assuming the same 1% accuracy, the faster P(Y) signal results in an accuracy of about 30 centimeters.

Electronics errors are one of several accuracy-degrading effects outlined in the table below. When taken together, autonomous civilian GPS horizontal position fixes are typically accurate to about 15 meters (50 ft). These effects also reduce the more precise P(Y) code's accuracy.

##### Atmospheric effects

Changing atmospheric conditions change the speed of the GPS signals as they pass through the Earth's atmosphere and ionosphere. Correcting these errors is a significant challenge to improving GPS position accuracy. These effects are minimized when the satellite is directly overhead, and become greater for satellites nearer the horizon, since the signal is affected for a longer time. Once the receiver's approximate location is known, a mathematical model can be used to estimate and compensate for these errors.

Because ionospheric delay affects the speed of radio waves differently based on frequency, a characteristic known as dispersion, both frequency bands can be used to help reduce this error. Some military and expensive survey-grade civilian receivers compare the different delays in the L1 and L2 frequencies to measure atmospheric dispersion, and apply a more precise correction. This can be done in civilian receivers without decrypting the P(Y) signal carried on L2, by tracking the carrier wave instead of the modulated code. To facilitate this on lower cost receivers, a new civilian code signal on L2, called L2C, was added to the Block IIR-M satellites, first launched in 2005. It allows a direct comparison of the L1 and L2 signals using the coded signal instead of the carrier wave.

The effects of the ionosphere are generally slow-moving, and can be averaged over time. The effects for any particular geographical area can be easily calculated by comparing the GPS-measured position to a known surveyed location. This correction is also valid for other receivers in the same general location. Several systems send this information over radio or other links to allow L1 only receivers to make ionospheric corrections. The ionospheric data are transmitted via satellite in Satellite Based Augmentation Systems such as WAAS, which transmits it on the GPS frequency using a special PRN, so only one antenna and receiver are required.

Humidity also causes a variable delay, resulting in errors similar to ionospheric delay, but occurring in the troposphere. This effect is much more localized, and changes more quickly than the ionospheric effects, making precise compensation for humidity more difficult. Altitude also causes a variable delay, as the signal passes through less atmosphere at higher elevations. Since the GPS receiver measures altitude directly, this is much simpler correction to apply.

Multipath effects

GPS signals can also be affected by multipath issues, where the radio signals reflect off surrounding terrain; buildings, canyon walls, hard ground, etc. These delayed signals can cause inaccuracy. A variety of techniques, most notably narrow correlator spacing, have been developed to mitigate multipath errors. For long delay multipath, the receiver itself can recognize the wayward signal and discard it. To address shorter delay multipath from the signal reflecting off the ground, specialized antennas may be used. Short delay reflections are harder to filter out since they are only slightly delayed, causing effects almost indistinguishable from routine fluctuations in atmospheric delay.

Multipath effects are much less severe in moving vehicles. When the GPS antenna is moving, the false solutions using reflected signals quickly fail to converge and only the direct signals result in stable solutions.

##### Ephemeris and clock errors

The navigation message from a satellite is sent out only every 12.5 minutes. In reality, the data contained in these messages tend to be "out of date" by an even larger amount. Consider the case when a GPS satellite is boosted back into a proper orbit; for some time following the maneuver, the receiver’s calculation of the satellite's position will be incorrect until it receives another ephemeris update. The onboard clocks are extremely accurate, but they do suffer from some clock drift. This problem tends to be very small, but may add up to 2 meters (6 ft) of inaccuracy.

This class of error is more "stable" than ionospheric problems and tends to change over days or weeks rather than minutes. This makes correction fairly simple by sending out a more accurate almanac on a separate channel.

##### Augmentation

Augmentation methods of improving accuracy rely on external information being integrated into the calculation process. There are many such systems in place and they are generally named or described based on how the GPS sensor receives the information. Some systems transmit additional information about sources of error (such as clock drift, ephemeris, or ionospheric delay), others provide direct measurements of how much the signal was off in the past, while a third group provide additional navigational or vehicle information to be integrated in the calculation process.

Examples of augmentation systems include the Wide Area Augmentation System, Differential GPS, and Inertial Navigation Systems.

Precise Monitoring

The accuracy of a calculation can also be improved through precise monitoring and measuring of the existing GPS signals in additional or alternate ways.

The first is called Dual Frequency monitoring, and refers to systems that can compare two or more signals, such as the L1 frequency to the L2 frequency. Since these are two different frequencies, they are affected in different, yet predictable ways by the atmosphere and objects around the receiver. After monitoring these signals, it is possible to calculate how much error is being introduced and then nullify that error.

Receivers that have the correct decryption key can relatively easily decode the P(Y)-code transmitted on both L1 and L2 to measure the error. Receivers that do not possess the key can still use a process called codeless to compare the encrypted information on L1 and L2 to gain much of the same error information. However, this technique is currently limited to specialized surveying equipment. In the future, additional civilian codes are expected to be transmitted on the L2 and L5 frequencies. When these become operational, non-encrypted users will be able to make the same comparison and directly measure some errors.

A second form of precise monitoring is called Carrier-Phase Enhancement (CPGPS). The error, which this corrects, arises because the pulse transition of the PRN is not instantaneous, and thus the correlation (satellite-receiver sequence matching) operation is imperfect. The CPGPS approach utilizes the L1 carrier wave, which has a period 1000 times smaller than that of the C/A bit period, to act as an additional clock signal and resolve the uncertainty. The phase difference error in the normal GPS amounts to between 2 and 3 meters (6 to 10 ft) of ambiguity. CPGPS working to within 1% of perfect transition reduces this error to 3 millimeters (1 inch) of ambiguity. By eliminating this source of error, CPGPS coupled with DGPS normally realizes between 20 and 30 centimeters (8 to 12 inches) of absolute accuracy.

Relative Kinematic Positioning (RKP) is another approach for a precise GPS-based positioning system. In this approach, determination of range signal can be resolved to an accuracy of less than 10 centimeters (4 in). This is done by resolving the number of cycles in which the signal is transmitted and received by the receiver. This can be accomplished by using a combination of differential GPS (DGPS) correction data, transmitting GPS signal phase information and ambiguity resolution techniques via statistical tests — possibly with processing in real-time (real-time kinematic positioning, RTK).

##### GPS Time

Atomic clocks on the satellites are set to "GPS time", similar to most time standards, but not corrected to the rotation of the Earth, ignoring leap seconds and other corrections. GPS time was set to match Coordinated Universal Time (UTC) in 1980, but has since diverged as leap seconds were added to UTC.

The current date is expressed in the GPS signal as a week number and a day-of-week number. GPS week zero started at 00:00:00 UTC (00:00:19 TAI) on January 6, 1980. The week number is transmitted in a ten-bit field, and so it wraps round every 1,024 weeks, (19.7 years). The transmitted week number rolled over to zero at 00:00:19 TAI on August 22, 1999 (23:59:47 UTC on August 21, 1999). GPS receivers thus need to know the time to within 3,584 days in order to correctly interpret the GPS date signal. A new field is being added to the GPS navigation message that specifies the calendar year number exactly, in a sixteen-bit field.

The GPS navigation message includes the difference between GPS time and UTC, which is 14 seconds as of 2006. Receivers subtract this offset from GPS time to calculate UTC and 'local' time. New GPS units may not show the correct UTC time, or not attempt to show UTC time at all, until after receiving the UTC offset message for the first time. This is usually within 15 minutes after the unit achieves GPS lock. The GPS-UTC offset field is only eight bits, and so it wraps round every 256 leap seconds. At the current rate of change of the earth's rotation, the first wraparound of this field is projected to occur in the year 2330.

##### Selective availability

The GPS includes a feature called Selective Availability (SA) that introduces intentional errors between 0 meters and up to a hundred meters (300 ft) into the publicly available navigation signals, making it difficult to use for guiding long range missiles to precise targets. Additional accuracy was available in the signal, but in an encrypted form that was only available to the United States military, its allies and a few others, mostly government users.

SA typically added signal errors of up to about 10 meters (30 ft) horizontally and 30 meters (100 ft) vertically. The inaccuracy of the civilian signal was deliberately encoded so as not to change very quickly, for instance the entire eastern U.S. area might read 30 m off, but 30 m off everywhere and in the same direction. In order to improve the usefulness of GPS for civilian navigation, Differential GPS was used by many civilian GPS receivers to greatly improve accuracy.

During the Gulf War, the shortage of military GPS units and the wide availability of civilian ones among personnel resulted in a decision to disable Selective Availability. This was ironic, as SA had been introduced specifically for these situations, allowing friendly troops to use the signal for accurate navigation, while at the same time denying it to the enemy. But since SA was also denying the same accuracy to thousands of friendly troops, turning it off or setting it to a error of 0 meters (effectively the same thing) presented a clear benefit.

In the 1990s, the FAA started pressuring the military to turn off SA permanently. This would save the FAA millions of dollars every year in maintenance of their own radio navigation systems. The military resisted for most of the 1990s, but SA was eventually "discontinued"; the amount of error added was "set to zero"[7] in 2000 following an announcement by U.S. President Bill Clinton, allowing users access to an undegraded L1 signal. Per the directive, the induced error of SA was changed to add no error to the public signals (C/A code). Selective Availability is still a system capability of GPS, and error could be in theory reintroduced at any time. In practice, in view of the hazards and costs this would induce for US and foreign shipping, it is unlikely to be reintroduced, and various government agencies (e.g. [1]) have stated that it is not intended to be reintroduced.

The US military has developed the ability to locally deny GPS (and other navigation services) to hostile forces in a specific area of crisis without affecting the rest of the world or its own military systems.

##### GPS jamming

The U.S. Air Force conducted GPS jamming exercises in 2003 and they also have GPS anti-spoofing capabilities. In 2002, a detailed description of how to build a short range GPS L1 C/A jammer was published in Phrack issue 60  by an anonymous author. There has also been at least one well-documented case of unintentional jamming, tracing back to a malfunctioning TV antenna preamplifier. If stronger signals were generated intentionally, they could potentially interfere with aviation GPS receivers within line of sight.

According to John Ruley, of AVweb, "IFR pilots should have a fallback plan in case of a GPS malfunction".Receiver Autonomous Integrity Monitoring(RAIM), a feature of some aviation and marine receivers, is designed to provide a warning to the user if jamming or another problem is detected. GPS signals can also be interfered with by natural geomagnetic storms, predominantly at high latitudes.

The U.S. government believes that such jammers were also used occasionally during the 2001 war in Afghanistan. Some officials believe that jammers could be used to attract the precision-guided munitions towards non-combatant infrastructure; other officials believe that the jammers are completely ineffective. In either case, the jammers may be attractive targets for anti-radiation missiles. During the Iraq War, the U.S. military claimed to destroy a GPS jammer with a GPS-guided bomb.

##### Relativity

According to Einstein's Theory of relativity, because of their constant movement and height relative to the Earth Centered Inertial reference frame the clocks on the satellites are affected by their speed (special relativity) as well as their gravitational potential (general relativity). Friedwardt Winterberg predicted in 1955 that when observed from the Earth's reference frame, satellite clocks would be perceived as running at a slightly faster rate than clocks on the Earth's surface. For GPS satellites, this discrepancy is 38 microseconds per day. To account for this, the frequency standard on-board the satellites is set to run slightly slower than its desired frequency on Earth, at 10.22999999543 MHz instead of 10.23 MHz—a difference of 0.00000046% or about five parts per billion. The atomic clocks on board the GPS satellites are precisely tuned, making this a practical demonstration of the theory of relativity in a real-world system.

Another relativistic effect to be compensated for in GPS observation processing is the Sagnac effect. The GPS time scale is defined in an inertial system, but observations are processed in an ECEF (co-rotating) system, in which simultaneity is not uniquely defined. The Lorentz transformation between the two systems modifies the signal run time, a correction having opposite algebraic signs for satellites in the Eastern and Western celestial hemispheres. Ignoring this effect will produce an East-West offset in the absolute position solution on the order of tens of metres.[citation needed]

Neil Ashby presented in Physics Today (May 2002)  an account how these relativistic corrections are applied, and their orders of magnitude. The error introduced by relativistic effects can be as much as 15 meters. The GPS system also makes adjustments for the relativistic drift of the atomic clocks in the satellites. Parts of this correction are carried out in the satellites and parts in the receiver.

##### History & Timeline

The design of GPS is based partly on the similar ground-based radio navigation systems, such as LORAN developed in the early 1940s, and used during World War II. Additional inspiration for the GPS system came when the Soviet Union launched the first Sputnik in 1957. A team of U.S. scientists led by Dr. Richard B. Kershner were monitoring Sputnik's radio transmissions. They discovered that, because of the Doppler effect, the frequency of the signal being transmitted by Sputnik was higher as the satellite approached, and lower as it continued away from them. They realized that since they knew their exact location on the globe, they could pinpoint where the satellite was along its orbit by measuring the Doppler distortion.

The first satellite navigation system, Transit, used by the United States Navy, was first successfully tested in 1960. Using a constellation of five satellites, it could provide a navigational fix approximately once per hour. In 1967, the U.S. Navy developed the Timation satellite which proved the ability to place accurate clocks in space, a technology the GPS system relies upon. In the 1970s, the ground-based Omega Navigation System, based on signal phase comparison, became the first world-wide radio navigation system.

The first experimental Block-I GPS satellite was launched in February 1978. The GPS satellites were initially manufactured by Rockwell International and are now manufactured by Lockheed Martin.

In 1983, after Soviet interceptor aircraft shot down the civilian airliner KAL 007 in restricted Soviet airspace, killing all 269 people on board, Ronald Reagan announced that the GPS system would be made available for civilian uses once it was completed.

By 1985, ten more experimental Block-I satellites had been launched to validate the concept. The first modern Block-II satellite was launched on February 14, 1989.

In 1992, the 2nd Space Wing, which originally managed the system, was de-activated and replaced by the 50th Space Wing.

The system achieved initial operational capability by December 1993[17] A complete constellation of 24 satellites was in orbit by January 17, 1994.

In 1996, recognizing the importance of GPS to civilian users as well as military users, President Bill Clinton issued a policy directive[18] declaring GPS to be a dual-use system and establishing an Interagency GPS Executive Board to manage it as a national asset.

In 1998, Vice President Al Gore announced plans to upgrade GPS with two new civilian signals for enhanced user accuracy and reliability, particularly with respect to aviation safety.

On 2 May 2000, "Selective Availability" was discontinued,

allowing users outside the US military to receive a full quality signal.

In 2004, President George W. Bush updated the national policy,

replacing the board with the National Space-Based Positioning,

Navigation, and Timing Executive Committee.

The most recent launch was on 17 November 2006.

The oldest GPS satellite still in operation was launched in October 1990.

#### Applications

Military

- GPS allows accurate targeting of various military weapons including cruise missiles and precision-guided munitions. The satellites also carry nuclear detonation detectors, which form a major portion of the United States Nuclear Detonation Detection System. To help prevent GPS from being used in improvised weaponry, the US Government controls the export of civilian receivers. A US-based manufacturer can not generally export a receiver unless it has limits on the velocities and altitudes at which it will report position and speed information. A general speed limitation of 515 m/sec applies and no GPS unit can function at an altitude of 18 kilometers or above.

Navigation

- Automobiles can be equipped with GPS receivers at the factory or as after-market equipment. Units often display moving maps and information about location, speed, direction, and nearby streets and landmarks.

- Aircraft navigation systems usually display a "moving map" and are often connected to the autopilot for en-route navigation. Aviation-certified GPS receivers using technologies such as WAAS or LAAS to increase accuracy may also be used for some final approach and landing operations. Hand-held aviation-certified GPS receivers are often used in smaller general aviation aircraft. Glider pilots use GNSS Flight Recorders to log GPS data verifying their arrival at turn points in gliding competitions. Flight computers installed in many gliders also use GPS to compute wind speed aloft, and glide paths to waypoints such as alternate airports or mountain passes, to aid en route decision making for cross-country soaring.

- Boats and ships can use GPS to navigate all of the world's lakes, seas and oceans. Maritime GPS units include functions useful on water, such as “man overboard” (MOB) functions that allow instantly marking the location where a person has fallen overboard, which simplifies rescue efforts. GPS may be connected to the ships self-steering gear and Chartplotters using the NMEA 0183 interface. GPS can also improve the security of shipping traffic by enabling AIS.

- Heavy Equipment can use GPS in construction, mining and precision agriculture. The blades and buckets of construction equipment are controlled automatically in GPS-based machine guidance systems. Agricultural equipment may use GPS to steer automatically, or as a visual aid displayed on a screen for the driver. This is very useful for controlled traffic and row crop operations and when spraying. Harvesters with yield monitors can also use GPS to create a yield map of the paddock being harvested.

- Bicycles often use GPS in racing and touring. GPS navigation allows cyclists to plot their course in advance and follow this course, which may include quieter, narrower streets, without having to stop frequently to refer to separate maps. Some GPS receivers are specifically adapted for cycling with special mounts and housings.

- Hikers, climbers, and even ordinary pedestrians in urban or rural environments can use GPS to determine their position, with or without reference to separate maps. In isolated areas, the ability of GPS to provide a precise position can greatly enhance the chances of rescue when climbers or hikers are disabled or lost (if they have a means of communication with rescue workers).

- GPS equipment for the visually impaired is available. For more detailed information see the article GPS for the visually impaired

#### Surveying and Mapping

- Surveying - Survey-Grade GPS receivers can be used to position survey markers, buildings, and road construction. These units use the signal from both the L1 and L2 GPS frequencies. Even though the L2 code data are encrypted, the signal's carrier wave enables correction of some ionospheric errors. These dual-frequency GPS receivers typically cost US$10,000 or more, but can have positioning errors on the order of one centimeter or less when used in carrier phase differential GPS mode.

- Mapping and GIS - Mapping grade GPS receivers use the carrier wave data from only the L1 frequency, but have a precise crystal oscillator which reduces errors related to receiver clock jitter. This allows positioning errors on the order of one meter or less in real-time, with a differential GPS signal received using a separate radio receiver. By storing the carrier phase measurements and differentially post-processing the data, positioning errors on the order of 10 centimeters are possible with these receivers.

- Geophysics and geology - High precision measurements of crustal strain can be made with differential GPS by finding the relative displacement between GPS sensors. Multiple stations situated around an actively deforming area (such as a volcano or fault zone) can be used to find strain and ground movement. These measurements can then be used to interpret the cause of the deformation, such as a dike or sill beneath the surface of an active volcano.

## Other Uses

- Precise time reference - Many systems that must be accurately synchronized use GPS as a source of accurate time. GPS can be used as a reference clock for time code generators or NTP clocks. Sensors (for seismology or other monitoring application), can use GPS as a precise time source, so events may be timed accurately. TDMA communications networks often rely on this precise timing to synchronize RF generating equipment, network equipment, and multiplexers.

- Mobile Satellite Communications - Satellite communications systems use a directional antenna (usually a "dish") pointed at a satellite. The antenna on a moving ship or train, for example, must be pointed based on its current location. Modern antenna controllers usually incorporate a GPS receiver to provide this information.

- Emergency and Location-based services - GPS functionality can be used by emergency services to locate cell phones. The ability to locate a mobile phone is required in the United States by E911 emergency services legislation. However, as of September 2006 such a system is not in place in all parts of the country. GPS is less dependent on the telecommunications network topology than radiolocation for compatible phones. Assisted GPS reduces the power requirements of the mobile phone and increases the accuracy of the location. A phone's geographic location may also be used to provide location-based services including advertising, or other location-specific information.

- Location-based games - The availability of hand-held GPS receivers has led to games such as Geocaching, which involves using a hand-held GPS unit to travel to a specific longitude and latitude to search for objects hidden by other geocachers. This popular activity often includes walking or hiking to natural locations. Geodashing is an outdoor sport using waypoints.

- Aircraft passengers - Most airlines allow passenger use of GPS units on their flights, except during landing and take-off when other electronic devices are also restricted. Even though consumer GPS receivers have a minimal risk of interference, a few airlines disallow use of hand-held receivers during flight. Other airlines integrate aircraft tracking into the seat-back television entertainment system, available to all passengers even during takeoff and landing.

- Heading information - The GPS system can be used to determine heading information, even though it was not designed for this purpose. A "GPS compass’  uses a pair of antennas separated by about 50 cm to detect the phase difference in the carrier signal from a particular GPS satellite. Given the positions of the satellite, the position of the antenna, and the phase difference, the orientation of the two antennas can be computed. More expensive GPS compass systems use three antennas in a triangle to get three separate readings with respect to each satellite. A GPS compass is not subject to magnetic declination as a magnetic compass is, and doesn't need to be reset periodically like a gyrocompass. It is, however, subject to multipath effects.

- GPS tracking systems use GPS to determine the location of a vehicle, person, or pet and to record the position at regular intervals in order to create a log of movements. The data can be stored inside the unit, or sent to a remote computer by radio or cellular modem. Some systems allow the location to be viewed in real-time on the Internet with a web-browser.

- Weather Prediction Improvements - Measurement of atmospheric bending of GPS satellite signals by specialized GPS receivers in orbital satellites can be used to determine atmospheric conditions such as air density, temperature, moisture and electron density. Such information from a set of six micro-satellites, launched in April 2006, called the Constellation of Observing System for Meteorology, Ionosphere and Climate COSMIC has been proven to improve the accuracy of weather prediction models.

# Text boxes

A modern personal GPS receiver  and route manager  /indicator

A GPS satellite of the last ‘generation’